#### cd tum_simulator
source /opt/ros/kinetic/setup.bash
source devel/setup.bash
roslaunch cvg_sim_gazebo ardrone_testworld.launch
#### terminal command control
take off
rostopic pub -1 /ardrone/takeoff std_msgs/Empty
land
rostopic pub -1 /ardrone/land std_msgs/Empty
switch camera
rosservice call /ardrone/togglecam
## Running Keyboard
rosrun teleop_twist_keyboard teleop_twist_keyboard.py
motion
# fly forward
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 1.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

# fly backward
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: -1.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

# fly to left
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 1.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

# fly to right
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: -1.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

# fly up
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 1.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

# fly down
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: -1.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'

# counterclockwise rotation
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 1.0}}'

# clockwise rotation
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: -1.0}}'

# stop
rostopic pub -r 10 /cmd_vel geometry_msgs/Twist '{linear: {x: 0.0, y: 0.0, z: 0.0}, angular: {x: 0.0,y: 0.0,z: 0.0}}'
### Robot Sensor Monitoring
For observation you can use following commands:
# The output camera
rosrun image_view image_view image:=/ardrone/image_raw

# The front camera
rosrun image_view image_view image:=/ardrone/front/image_raw

# The buttom camera
rosrun image_view image_view image:=/ardrone/bottom/image_raw

# The height sensor
rostopic echo /sonar_height

#The navigation info
rostopic echo /ardrone/navdata

#A launch file for joystick drivers and image view nodes
roslaunch cvg_sim_test demo_tool.launch
OR using the rviz tool.
##### Cannot control drone via joystick
- check, whether you are using the correct joystick
- check, whether you joystick driver is running properly, and sending correct rostopics
rostopic echo /joy
check, whether the ardrone_joystick node is running properly by checking the following topics
rostopic echo /cmd_vel
rostopic echo /ardrone/land
rostopic echo /ardrone/reset
rostopic echo /ardrone/takeoff
##### The simulated ardrone